Total

Number of LUTs : 53200
Number of LUTRAM : 17400
FF : 106400
DSP : 220
IO : 200
BRAM : 140

1 8 bit 8-tap FIR filter

FIR Compiler

Number of LUTs : 32
Number of LUTRAM : 11
FF : 67
DSP : 1
IO : 20
Power 0.123 W
Critical Path : 7.224 ns

Takes 3 clock cycles to start

BRAM constant coefficient

Number of LUTs : 93
Number of LUTRAM : 28
FF : 244
DSP : 0
IO : 33
BRAM : 2
Power 0.138 W
Critical Path : 5.522 ns2

-- Name : Brenda So
-- Date : 11/4/2017
-- Goal : Make a processing engine (PE) block for convolution
-- follows systolic form with pipeline multiplier

library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;

-- Uncomment the following library declaration if using
-- arithmetic functions with Signed or Unsigned values
--use IEEE.NUMERIC_STD.ALL;

-- Uncomment the following library declaration if instantiating
-- any Xilinx leaf cells in this code.
--library UNISIM;
--use UNISIM.VComponents.all;

entity pe_block_1 is
  Port (
        clk: IN STD_LOGIC;
        x_in: IN SIGNED(7 downto 0);
        y_in: IN SIGNED(7 downto 0);
        x_out: OUT SIGNED(7 downto 0);
        y_out: OUT SIGNED(7 downto 0)
        );
end pe_block_1;

architecture RTL of pe_block_1 is

component mult_gen_1 IS
  port (
    A : IN STD_LOGIC_VECTOR(7 DOWNTO 0);
    P : OUT STD_LOGIC_VECTOR(7 DOWNTO 0)
  );
end component;

signal x_1: SIGNED(7 downto 0);
signal x_2: SIGNED(7 downto 0) ;
signal x_inter: STD_LOGIC_VECTOR(7 downto 0);
signal x_mult : STD_LOGIC_VECTOR(7 downto 0);
signal x_mult_d : SIGNED(7 downto 0);
signal x_add : SIGNED(7 downto 0);

begin
mult_1 : mult_gen_1 port map(A=>x_inter, P=>x_mult);
process(clk)
begin
    if rising_edge(clk) then
        -- shift the shift registers
        x_1 <= x_in;
        x_2 <= x_1;
        x_inter <= std_logic_vector(x_2);
        x_out <= x_2;
        --- multiplication
        x_mult_d <= signed(x_mult);
        x_add <= x_mult_d + y_in;
        y_out <= x_add;
    end if;
end process;

end RTL;